## Slide 1
Lesson 1
How are plastics made?
Ocean Plastics
Design and Technology | 11-14

## Slide 2: Lesson 1: How are plastics made?
List all the things we can do, and make, with oil...

## Slide 3: Lesson 1: How are plastics made?
State that plastics are made from oil.
Describe the steps involved in making plastic.
State what a monomer and a polymer is.
Describe how changing a substance’s structure can change its properties

## Slide 4: Lesson 1: How are plastics made?
How might we turn oil into a hard plastic?

## Slide 5: Lesson 1: How are plastics made?
Move around the room and discover how are plastics made…

## Slide 6: Lesson 1: How are plastics made?
Recap steps

## Slide 7: Lesson 1: How are plastics made?
What have we changed to make oil become plastic?

## Slide 8: Lesson 1: How are plastics made?
Mono = one
Poly = many
A monomer is an individual unit. A polymer is a chain of the same monomers chemically bonded. When many monomers chemically join to form a polymer, we call this polymerisation.
H
H
H
H
C
C
H
H
H
H
H
H
H
H
H
H
H
H
H
H
C
C
C
C
C
C
H
H
H
H
C
C
H
H
H
H
C
C
Monomers
Polymer
Monomers & Polymers

## Slide 9: Lesson 1: How are plastics made?
Thermoplastic:
Consists of long polymer chains with few cross-links.
This means when heated it becomes soft and can be reshaped. When cooled it returns solid again.
Thermosetting plastic:
Consists of long, heavy chains with many cross-link chains.
Soft when first made. But once set they are very stiff and can not be heated and reshaped.
Plastic polymer chain
Cross-link
Plastic polymer chain
Cross-link
Thermoplastic vs Thermosetting Plastics

## Slide 10: Lesson 1: How are plastics made?
Arrange the materials into two categories: thermoplastic and thermosetting plastics
Thermosetting plastics
Thermoplastics
Thermoplastic vs Thermosetting Plastics

## Slide 11: Lesson 1: How are plastics made?
Arrange the materials into two categories: thermoplastic and thermosetting plastics
Thermoplastic vs Thermosetting Plastics
Thermosetting
Epoxy resin (ER)
Melamine formaldehyde (MF)
Polyester resin (PR)
Urea formaldehyde (UF)
Phenol formaldehyde (PF)
Thermoplastics
Polypropylene (PP)
Polyethylene (PET)
Polycarbonate (PC)
Polyamide (Nylon)
High impact polystyrene (HIP)

## Slide 12: Lesson 1: How are plastics made?
How does it work?
PVA is a polymer. The borax goes in between the polymer strands and connects them. Therefore they act like longer chains. This gives slime a new texture.
PVA
Borax
Method:
Fill a cup with ½ inch of glue
Add 2 table spoons of water
Add food colouring
Add 2 table spoons of borax powder
Stir very well
Leave to rest for 1 minute
Making Slime

## Slide 13: Lesson 1: How are plastics made?
Write down:
1 thing you loved
1 thing you would bin
1 thing you will recycle
Reflection

## Slide 14: Lesson 1: How are plastics made?
Find 5 products at home made of plastic.
Photograph the symbols printed or etched on to the plastic.
Bring an A4 sized sheet of the photographs.
Add a key stating what these symbols mean.
Home Learning
Notes: There is information available to help students complete this task on page 6 of our Plastic Clever Schools Workbook https://plasticcleverschools.co.uk/wp-content/uploads/2023/06/PCS_-_SECONDARY_Student_Workbook_Feb_2023_SCREEN_AW.pdf

## Slide 15: Lesson 1: How are plastics made?
Image credits
All other images are courtesy of Encounter Edu
Slide | Title | Attribution
1 | Plastic bottles | By Itsanan via Bigstock
4, 7 | Crude oil | By Glasbruch 2007 via Wikimedia
5 | Plastic pellets | By Feiern1 via Pixabay

## Slide 16: Lesson 1: How are plastics made?
Oil rig
Oil rigs can be found on land and at sea. They drill down and remove crude oil from the ground. Crude oil is a mixture of many substances, but most important are the hydrocarbons (molecules made of hydrogen and carbon).

## Slide 17: Lesson 1: How are plastics made?
Oil refinery
1. Fractional distillation
The parts of crude oil can be separated out through a process called fractional distillation.
The crude oil is heated until it vaporizes. It is put into a column where the different oils separate out.
2. Cracking
During cracking, Naptha oil is broken down from a 10-carbon chain molecule to many 2-carbon chain molecules.

## Slide 18: Lesson 1: How are plastics made?
Chemical factory
Polymerisation
The smaller 2 carbon chain molecules are monomers. Now these 2 chain molecules are rejoined to make very long chains called polymers. This is done using a catalyst.
2. Chemical additives
Plasticisers and other chemicals are added to improve the quality of the plastic. These can change the material’s colour, flexibility, and stability to heat.

## Slide 19: Lesson 1: How are plastics made?
Pellets
The plastic pellets are made of hydrocarbon chains and chemical additives.
These pellets can be shipped to factories across the world to create lots of different products

## Slide 20: Lesson 1: How are plastics made?
Moulding
The pellets are heated. The plastic becomes a soft resin which can be injected into moulds. The resin cools and is released from the mould. The plastic now has the desired shape.